## Slide 1: Digital Design & Computer Arch. Lecture 14: Pipelining Issues
Prof. Onur Mutlu
ETH Zürich
Spring 2020
3 April 2020

## Slide 2: Required Readings
This week
  Pipelining
    H&H, Chapter 7.5
  Pipelining Issues
    H&H, Chapter 7.8.1-7.8.3
Next week
  Out-of-order execution
    H&H, Chapter 7.8-7.9
  Smith and Sohi, “The Microarchitecture of Superscalar Processors,” Proceedings of the IEEE, 1995
    More advanced pipelining
    Interrupt and exception handling
    Out-of-order and superscalar execution concepts

## Slide 3: Agenda for Today & Next Few Lectures
Last week
  Single-cycle Microarchitectures
  Multi-cycle Microarchitectures
This week
  Pipelining
  Issues in Pipelining: Control & Data Dependence Handling, State Maintenance and Recovery, …
Next week
  Out-of-Order Execution
  Issues in OoO Execution: Load-Store Handling, …

## Slide 4: Review: How to Handle Data Dependences
Anti and output dependences are easier to handle
  write to the destination in one stage and in program order
Flow dependences are more interesting
Six fundamental ways of handling flow dependences
  Detect and wait until value is available in register file
  Detect and forward/bypass data to dependent instruction
  Detect and eliminate the dependence at the software level
    No need for the hardware to detect dependence
  Detect and move it out of the way for independent instructions
  Predict the needed value(s), execute “speculatively”, and verify
  Do something else (fine-grained multithreading)
    No need to detect

## Slide 5: Stalling

## Slide 6: Stalling Hardware
Stalls are supported by:
  adding enable inputs (EN) to the Fetch and Decode pipeline registers
  and a synchronous reset/clear (CLR) input to the Execute pipeline register
    or an INV bit associated with each pipeline register
When a lw stall occurs
  StallD and StallF are asserted to force the Decode and Fetch stage pipeline registers to hold their old values.
  FlushE is also asserted to clear the contents of the Execute stage pipeline register, introducing a bubble

## Slide 7: Stalling Hardware

## Slide 8: Control Dependences
Special case of data dependence: dependence on PC
beq:
  branch is not determined until the fourth stage of the pipeline
  Instructions after the branch are fetched before branch is resolved
    Always predict that the next sequential instruction is fetched
    Called “Always not taken” prediction
  These instructions must be flushed if the branch is taken
Branch misprediction penalty
  number of instructions flushed when branch is taken
  May be reduced by determining branch earlier

## Slide 9: Control Dependence: Original Pipeline

## Slide 10: Control Dependence

## Slide 11: Early Branch Resolution
Introduces another data dependency in Decode stage..

## Slide 12: Early Branch Resolution

## Slide 13: Early Branch Resolution: Good Idea?
Advantages
  Reduced branch misprediction penalty
     Reduced CPI (cycles per instruction)
Disadvantages
  Potential increase in clock cycle time?
     Higher Tclock?
  Additional hardware cost
     Specialized and likely not used by other instructions

## Slide 14: Data Forwarding for Early Branch Resolution
Data forwarding for early branch resolution.

## Slide 15: Control Forwarding and Stalling Hardware
// Forwarding logic:
assign ForwardAD = (rsD != 0) & (rsD == WriteRegM) & RegWriteM; assign ForwardBD = (rtD != 0) & (rtD == WriteRegM) & RegWriteM;
//Stalling logic:
assign lwstall = ((rsD == rtE) | (rtD == rtE)) & MemtoRegE;
assign branchstall = (BranchD & RegWriteE & (WriteRegE == rsD | WriteRegE == rtD)) |
(BranchD & MemtoRegM &
(WriteRegM == rsD | WriteRegM == rtD));
// Stall signals;
assign StallF = lwstall | branchstall;
assign StallD = lwstall | branchstall;
assign FLushE = lwstall | branchstall;

## Slide 16: Doing Better: Smarter Branch Prediction
Guess whether branch will be taken
  Backward branches are usually taken (loops)
  Consider history of whether branch was previously taken to improve the guess
Good prediction reduces the fraction of branches requiring a flush

## Slide 17: Pipelined Performance Example
SPECINT2006 benchmark:
  25% loads
  10% stores
  11% branches
  2% jumps
  52% R-type
Suppose:
  40% of loads used by next instruction
  25% of branches mispredicted
All jumps flush next instruction
What is the average CPI?

## Slide 18: Pipelined Performance Example Solution
Load/Branch CPI = 1 when no stall/flush, 2 when stall/flush. Thus:
  CPIlw = 1(0.6) + 2(0.4) = 1.4 Average CPI for load
  CPIbeq = 1(0.75) + 2(0.25) = 1.25 Average CPI for branch
And
  Average CPI =

## Slide 19: Pipelined Performance Example Solution
Load/Branch CPI = 1 when no stall/flush, 2 when stall/flush. Thus:
  CPIlw = 1(0.6) + 2(0.4) = 1.4 Average CPI for load
  CPIbeq = 1(0.75) + 2(0.25) = 1.25 Average CPI for branch
And
  Average CPI = (0.25)(1.4) + load (0.1)(1) + store (0.11)(1.25) + beq (0.02)(2) + jump (0.52)(1) r-type = 1.15

## Slide 20: Pipelined Performance
There are 5 stages, and 5 different timing paths:
Tc = max { tpcq + tmem + tsetup fetch 2(tRFread + tmux + teq + tAND + tmux + tsetup ) decode tpcq + tmux + tmux + tALU + tsetup execute tpcq + tmemwrite + tsetup memory 2(tpcq + tmux + tRFwrite) writeback }
The operation speed depends on the slowest operation
Decode and Writeback use register file and have only half a clock cycle to complete, that is why there is a 2 in front of them

## Slide 21: Pipelined Performance Example
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Equality comparator | teq | 40
AND gate | tAND | 15
Memory write | Tmemwrite | 220
Register file write | tRFwrite | 100
Tc = 2(tRFread + tmux + teq + tAND + tmux + tsetup ) = 2[150 + 25 + 40 + 15 + 25 + 20] ps = 550 ps

## Slide 22: Pipelined Performance Example
For a program with 100 billion instructions executing on a pipelined MIPS processor:
  CPI = 1.15
  Tc = 550 ps
Execution Time = (# instructions) × CPI × Tc = (100 × 109)(1.15)(550 × 10-12) = 63 seconds

## Slide 23: Performance Summary for MIPS arch.
Processor | Execution Time (seconds) | Speedup (single-cycle is baseline)
Single-cycle | 95 | 1
Multicycle | 133 | 0.71
Pipelined | 63 | 1.51
Fastest of the three MIPS architectures is Pipelined.
However, even though we have 5 fold pipelining, it is not 5 times faster than single cycle.

## Slide 24: Questions to Ponder
What is the role of the hardware vs. the software in data dependence handling?
  Software based interlocking
  Hardware based interlocking
  Who inserts/manages the pipeline bubbles?
  Who finds the independent instructions to fill “empty” pipeline slots?
  What are the advantages/disadvantages of each?
    Think of the performance equation as well

## Slide 25: Questions to Ponder
What is the role of the hardware vs. the software in the order in which instructions are executed in the pipeline?
  Software based instruction scheduling  static scheduling
  Hardware based instruction scheduling  dynamic scheduling
How does each impact different metrics?
  Performance (and parts of the performance equation)
  Complexity
  Power consumption
  Reliability
  …

## Slide 26: More on Software vs. Hardware
Software based scheduling of instructions  static scheduling
  Compiler orders the instructions, hardware executes them in that order
  Contrast this with dynamic scheduling (in which hardware can execute instructions out of the compiler-specified order)
  How does the compiler know the latency of each instruction?
What information does the compiler not know that makes static scheduling difficult?
  Answer: Anything that is determined at run time
    Variable-length operation latency, memory addr, branch direction
How can the compiler alleviate this (i.e., estimate the unknown)?
  Answer: Profiling

## Slide 27: Pipelining and Precise Exceptions: Preserving Sequential Semantics

## Slide 28: Multi-Cycle Execution
Not all instructions take the same amount of time for “execution”
Idea: Have multiple different functional units that take different number of cycles
  Can be pipelined or not pipelined
  Can let independent instructions start execution on a different functional unit before a previous long-latency instruction finishes execution
F
D
E
?
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store

## Slide 29: Issues in Pipelining: Multi-Cycle Execute
Instructions can take different number of cycles in EXECUTE stage
  Integer ADD versus FP MULtiply
  What is wrong with this picture in a Von Neumann architecture?
    Sequential semantics of the ISA NOT preserved!
    What if FMUL incurs an exception?
F
D
E
W
F
D
E
W
E
E
E
E
E
E
E
FMUL R4  R1, R2
ADD R3  R1, R2
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
FMUL R2  R5, R6
ADD R7  R5, R6
F
D
E
W
E
E
E
E
E
E
E

## Slide 30: Exceptions vs. Interrupts
Cause
  Exceptions: internal to the running thread
  Interrupts: external to the running thread
When to Handle
  Exceptions: when detected (and known to be non-speculative)
  Interrupts: when convenient
    Except for very high priority ones
      Power failure
      Machine check (error)
Priority: process (exception), depends (interrupt)
Handling Context: process (exception), system (interrupt)

## Slide 31: Precise Exceptions/Interrupts
The architectural state should be consistent (precise) when the exception/interrupt is ready to be handled
1. All previous instructions should be completely retired.
2. No later instruction should be retired.
Retire = commit = finish execution and update arch. state

## Slide 32: Checking for and Handling Exceptions in Pipelining
When the oldest instruction ready-to-be-retired is detected to have caused an exception, the control logic
  Ensures architectural state is precise (register file, PC, memory)
  Flushes all younger instructions in the pipeline
  Saves PC and registers (as specified by the ISA)
  Redirects the fetch engine to the appropriate exception handling routine

## Slide 33: Why Do We Want Precise Exceptions?
Semantics of the von Neumann model ISA specifies it
  Remember von Neumann vs. Dataflow
Aids software debugging
Enables (easy) recovery from exceptions
Enables (easily) restartable processes
Enables traps into software (e.g., software implemented opcodes)

## Slide 34: Ensuring Precise Exceptions in Pipelining
Idea: Make each operation take the same amount of time
Downside
  Worst-case instruction latency determines all instructions’ latency
  What about memory operations?
  Each functional unit takes worst-case number of cycles?
F
D
E
W
F
D
E
W
E
E
E
E
E
E
E
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
FMUL R3  R1, R2
ADD R4  R1, R2

## Slide 35: Solutions
Reorder buffer
History buffer
Future register file
Checkpointing
Suggested reading
  Smith and Plezskun, “Implementing Precise Interrupts in Pipelined Processors,” IEEE Trans on Computers 1988 and ISCA 1985.
We will not cover these

## Slide 36: Recall: Solution I: Reorder Buffer (ROB)
Idea: Complete instructions out-of-order, but reorder them before making results visible to architectural state
When instruction is decoded it reserves the next-sequential entry in the ROB
When instruction completes, it writes result into ROB entry
When instruction oldest in ROB and it has completed without exceptions, its result moved to reg. file or memory
Register
File
Func Unit
Func Unit
Func Unit
Reorder
Buffer
Instruction
Cache

## Slide 37: Reorder Buffer
Buffers information about all instructions that are decoded but not yet retired/committed

## Slide 38: What’s in a ROB Entry?
Everything required to:
  correctly reorder instructions back into the program order
  update the architectural state with the instruction’s result(s), if instruction can retire without any issues
  handle an exception/interrupt precisely, if an exception/interrupt needs to be handled before retiring the instruction
Need valid bits to keep track of readiness of the result(s) and find out if the instruction has completed execution
V
DestRegID
DestRegVal
StoreAddr
StoreData
PC
Valid bits for reg/data + control bits
Exception?

## Slide 39: Reorder Buffer: Independent Operations
Result first written to ROB on instruction completion
Result written to register file at commit time
What if a later instruction needs a value in the reorder buffer?
  One option: stall the operation  stall the pipeline
  Better: Read the value from the reorder buffer. How?
F
D
E
W
F
D
E
R
E
E
E
E
E
E
E
F
D
E
W
F
D
E
R
F
D
E
R
F
D
E
R
F
D
E
R
E
E
E
E
E
E
E
W
R
R
W
W
W
W

## Slide 40: Reorder Buffer: How to Access?
A register value can be in the register file, reorder buffer, (or bypass/forwarding paths)
Register
File
Func Unit
Func Unit
Func Unit
Reorder
Buffer
Instruction
Cache
bypass paths
Content
Addressable
Memory
(searched with
register ID,
which is part of the content of an entry)
Random Access Memory
(indexed with Register ID,
which is the address of an entry)

## Slide 41: Simplifying Reorder Buffer Access
Idea: Use indirection
Access register file first (check if the register is valid)
  If register not valid, register file stores the ID of the reorder buffer entry that contains (or will contain) the value of the register
  Mapping of the register to a ROB entry: Register file maps the register to a reorder buffer entry if there is an in-flight instruction writing to the register
Access reorder buffer next
Now, reorder buffer does not need to be content addressable

## Slide 42: Reorder Buffer in Intel Pentium III
Boggs et al., “The Microarchitecture of the Pentium 4 Processor,” Intel Technology Journal, 2001.

## Slide 43: Important: Register Renaming with a Reorder Buffer
Output and anti dependencies are not true dependencies
  WHY? The same register refers to values that have nothing to do with each other
  They exist due to lack of register ID’s (i.e. names) in the ISA
The register ID is renamed to the reorder buffer entry that will hold the register’s value
  Register ID  ROB entry ID
  Architectural register ID  Physical register ID
  After renaming, ROB entry ID used to refer to the register
This eliminates anti and output dependencies
  Gives the illusion that there are a large number of registers

## Slide 44: Recall: Data Dependence Types
True (flow) dependence
      r3  r1 op r2 Read-after-Write
      r5  r3 op r4 (RAW) -- True
Anti dependence
      r3  r1 op r2 Write-after-Read
      r1  r4 op r5 (WAR) -- Anti
Output-dependence
      r3  r1 op r2 Write-after-Write
      r5  r3 op r4 (WAW) -- Output
      r3  r6 op r7

## Slide 45: Renaming Example
Assume
  Register file has a pointer to the reorder buffer entry that contains or will contain the value, if the register is not valid
  Reorder buffer works as described before
Where is the latest definition of R3 for each instruction below in sequential order?
  LD R0(0)  R3
  LD R3, R1  R10
  MUL R1, R2  R3
  MUL R3, R4  R11
  ADD R5, R6  R3
  ADD R7, R8  R12

## Slide 46: In-Order Pipeline with Reorder Buffer
Decode (D): Access regfile/ROB, allocate entry in ROB, check if instruction can execute, if so dispatch instruction
Execute (E): Instructions can complete out-of-order
Completion (R): Write result to reorder buffer
Retirement/Commit (W): Check for exceptions; if none, write result to architectural register file or memory; else, flush pipeline and start from exception handler
In-order dispatch/execution, out-of-order completion, in-order retirement
F
D
E
W
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
. . .
Integer add
Integer mul
FP mul
Load/store
R
R

## Slide 47: Reorder Buffer Tradeoffs
Advantages
  Conceptually simple for supporting precise exceptions
  Can eliminate false dependences
Disadvantages
  Reorder buffer needs to be accessed to get the results that are yet to be written to the register file
    CAM or indirection  increased latency and complexity
Other solutions aim to eliminate the disadvantages
  History buffer
  Future file
  Checkpointing
We will not cover these

## Slide 48: Digital Design & Computer Arch. Lecture 14: Pipelining Issues
Prof. Onur Mutlu
ETH Zürich
Spring 2020
3 April 2020